## Slide 1: Recipe control

## Slide 2: Recipe Control:
Production Engineer is able to:
Configure production sequence
Setup batch data recording
Production planing
Produce products with different options

## Slide 3: Educational Goasl
You can explain the major concepts of recipe control
You can configure a recipe
You know how to use general transition conditions

## Slide 4: Topics
Model for plant control
Equipment module control
Recipe control

## Slide 5: Physical Model

## Slide 6: Control module
Control of a device
Example:
  Motor control
  Servo feedback control
  Sensor

## Slide 7: Equipment module control
functional group of equipment that can carry out a finite number of specific processing activities.
Control unit of a modular plant
Know-How ‚entity‘
Testable unit

## Slide 8: Unit Control
A unit is a collection of Equipment Modules that can carry out one or more processing activities
Usually a recipe execution system

## Slide 9: Process Cell Control
Coordination of Units

## Slide 10: Example

## Slide 11: Recipe Control
Recipe Interface!

## Slide 12: Documentation of equipment module control
Build Classes!
Define common operation modes
Simplify safety functionality
Define general go-on condition, i.e. sensible for all operation modes

## Slide 13: Example: Temperatur Control
 | Processparameter |  | 
Operation Mode A | Description | active Devices | GoOn Condition
0: Off | not active | no | TRUE
1: Wall T- Control | The temperature feedback controller regulates wall temperature Tx.2 to setpoint (Par 3) | T-Control Valve TV x.5.1 - 4 | TRUE if T is in range for 5 min
2: Reactor T- Control | The temperature feedback controller regulates reactor temperature Tx.1 to setpoint (Par 3) using a cascaded control structure with wall temperatur control. | T-Control Valve TV x.5.1 - 4 | TRUE if T in range for 5 min
3: Reactor T-Control, T limitation | The temperature feedback controller regulates reactor temperature Tx.1 to setpoint (Par 3) using a cascaded control structure with wall temperatur control. Setpoint of the wall temperature controller is limited to [Tx.1 - T ... Tx.2 + T]. (T: Par 4) | T-Control Valve TV x.5.1 - 4 | TRUE if T in range for 5 min
4: Ramped Reactor T- Control | The temperature feedback controller regulates reactor temperature Tx.1 to setpoint (Par 3) using a cascaded control structure with wall temperatur control. Setpoint of the reaktor temperature controller is ramped with Ramp velocity(Par 5) | T-Control Valve TV x.5.1 - 4 | TRUE if T in range for 5 min and final value is attained

## Slide 14: A Recipe

## Slide 15: Recipe modells
Goal:
Plant and Site independent Recipes
Site dependent variations are possible

## Slide 16: Recipe Model

## Slide 17: Recipe model